## Slide 1: ED Induction – Common ED Equipment & Procedures
Mr. Robert Ritchie – Emergency Medicine Consultant
Pg Cert (Clin Sup), Dip Mgnt (Leicester), MBBS, FRCS, FFAEM, Member of ACEP
Dr. Niri Pinto – ST3 Emergency Medicine Registrar
MBBS, MRCEM

## Slide 2: Common ED Equipment & Procedures
List as many ED equipment on next slide
National Safety, HSE, and Professional Code of practice

## Slide 4: Common ED Equipment & Procedures
(Multi-functional) Cardiac monitor
  BP machine
  ECG
  O-2 & CO-2 monitors, etc
Defibrillator
Thermometer
Wall equipment (ENT, supplies, PPE, etc)
Work-table / Stationery
Light source and bed / trolley
Next room equipment
  Urine dip
  Urine b-HCG
  BM/ Ketone machine
  Blood gas machine ABG/ VBG
Infection control & Janitorial equipment
Anaesthetic Equipment
In Drawers
  Phlebotomy and dressing equipment
  Medications / Fluids/ Wound care

## Slide 5: Common ED Equipment & Procedures
Some Common procedures
Slit lamp examination
Plastering
C-spine immobilization / Traction
Joint reduction
Haematoma block
FB removal
IFCB / Femoral Block
U/S guided vascular access
ABG
Dressings
  Wounds
  Types
  Tissue Viability Nurse (TVN) service
Sutures
  Courses
  Web sites

## Slide 6: Common ED Equipment & Procedures
Non invasive BP measurement involves the application of pressure cuff
  Manual (listening for Kortokoff sounds)
  Automatic
  Electronic
    IR
    Thermocouple
    “Diagnostic table”
Platysmogram method
BP measuring artefacts
Safe practice

## Slide 7: Common ED Equipment & Procedures
Non invasive BP machine – The How to
Appropriately sized cuff to upper arm
  Near level of heart
Push start
Cuff inflated above systolic then incrementally deflated
  Amplitudes of cuff pressure oscillations measured by a pressure transducer
  Amplitudes start to increase to 25-50% of maximum  systolic
  Point of maximum oscillation MAP (most reliable measurement)
  Amplitudes decrease by 80% or disappear diastolic
Notes: Disadvantages of the oscillometric method
inaccurate: the 95% confidence interval for blood pressure in the normal range is +/- 15mmHg!
can’t be easily calibrated
inaccurate hypovolaemic
cuff small -> high BP
can’t be used in helicopter
Underestimates high blood pressures
Overestimates low blood pressure
the accuracy is even worse if dysrhythmia is present
COMPLICATIONS
arrhythmias
muscle tremors
pain, limb oedema, nerve trauma

## Slide 8: Common ED Equipment & Procedures
The ECG machine limitations
Patient, Equipment, and Operator Limitations
Anatomical considerations  Obesity, chest size, location of the heart, lung disease, effusions
Movement during the test  movement artefacts (e.g. Parkinson’s)
Exercise or smoking before the test
Electrolyte imbalances
Some common errors on chest lead placements
Wrong intercostal space
Placing lead on breast
Using different ECG machines on the same patient
Infection control
Hirsute patient
Certain medicines

## Slide 9: Common ED Equipment & Procedures
  The ECG machine
  Electrodes attached to the chest and/or limbs record
    Small voltage changes as potential difference,
      Transposed into a visual tracing

## Slide 10: Common ED Equipment & Procedures
Lead Views
Limb leads look from a ‘vertical plane’
I and AVL look from the left side - lateral wall
II, III and AVF look up from the bottom of the heart – inferior wall
AVR looks from the right, but use that to tell you if the leads are on wrongly or Dextrocardia!

## Slide 11: Common ED Equipment & Procedures
Lead Placement
Limb leads – Ride Your Green Bike!
V1- 4th intercostal space to the right of sternum
V2- As above but to the left
V3- Midway between V2 and V4 (do V4 first)
V4- Mid clavicular, 5th intercostal space
V5- Anterior axillary line, horizontal to V4
V6- Mid axillary line, horizontal to V4 and V5
Shave excess hair
use sub-mammary line for female
For limb leads place at wrists and close to ankle
If patient shaking, go for bony areas

## Slide 12: Common ED Equipment & Procedures
Right Sided and Posterior ECGs
Right sided
  Inferior MI
  Children
  Dextrocardia
Could change management of hypotension in post MI patient
Look for ST elevation in rV4
Ensure ECG strip is clearly labelled
Posterior ECG – may not change treatment

## Slide 13
3-electrode system
3 electrodes (RA, LA and LL)
Monitor displays the bipolar leads (I, II and III)
Best results – Electrodes equidistant from the heart (rather than the specific limbs)
5-electrode system
5 electrodes (RA, RL, LA, LL and Chest)
Monitor displays the bipolar leads (I, II and III)
  AND a single unipolar lead (depending on position of the brown chest lead (positions V1–6))
Common ED Equipment & Procedures

## Slide 14
12-lead ECG
10 electrodes to produce 12-lead ECG
  4 Electrodes on all 4 limbs (RA, LL, LA, RL)
  6 Electrodes on precordium (V1–6)
Monitors 12 leads (V1–6), (I, II, III) and (aVR, aVF, aVL)
Identify specific areas of the heart
  Inferior (II, III, aVF)
  Lateral (I, aVL, V5, V6)
  Anterior (V1–4)
12-lead Precordial lead placement
  V1: Rt. Parasternal 4th intercostal space V2: Lt. parasternal intercostal
  V4: 5th ICS, mid-clavicular line
  V3: midway between V2 and V4
  V5: 5th ICS, anterior axillary line (same level as V4)
  V6: 5th ICS, mid-axillary line (same level as V4)
Common ED Equipment & Procedures

## Slide 15: Cardiac Monitor - Show and tell
Common ED Equipment & Procedures

## Slide 16: Cardiac Monitor - Show and tell
Common ED Equipment & Procedures
Multi-mode ECG
SpO2
Non invasive BP
CO2 Capnograph
Power
Additional ports e.g. Arterial BP, Temp,

## Slide 17: Common ED Equipment & Procedures
Monitor
Multi-mode
3-lead, 5-lead, and 12-lead
Some calibrate to measure Resp Rate
BP
ECG monitor and trace
Remote links uses HL-7 format
O-2 sat
CO-2
Transducer
Temperature thermocouple
Internet / remote links

## Slide 18: Common ED Equipment & Procedures
Pulse oximeter
Diodes produce light red + infra-red
Photodetector - on opposite side of probe; detects transmitted light
Signal converter
  DC component  tissue + capillary blood + venous blood & non pulsatile arterial blood flow
  AC component  pulsatile arterial blood flow
  DC component is subtracted
  AC component is amplified and averaged over few seconds
Display - Signal is displayed as
  Continuous trace
  Graph
  Table
Notes: Pulse Oximeter • LITFL • CCC Equipment

## Slide 19: Common ED Equipment & Procedures
Pulse oximeter Limitations
  SpO2 and SaO2 are not measures of blood or tissue oxygenation
  (if [Hb] and cardiac output known, then oxygen delivery (DO2) can be calculated from SaO2)
  insensitive to directional changes in PaO2 above 80mmHg
  relatively insensitive to perfusion due to gain
  reading failure
  lag time (around 1 minute)
  Artefacts and error (using the wrong probe on the wrong site

## Slide 20: Common ED Equipment & Procedures
Pulse oximeter – Some Sources of Error
Motion artefact
Signal to noise ratio (shocked, hypothermia, vasoconstrictors)
Dyshaemoglobinaemias (COHb indistinguishable from HbO2, Met Hb absorbance high -> R = 1.0)
Anaemia
Intravenous dyes
Nail polish
Abnormal pulses (venous waves and ventilation)
Probe position
Low saturations (progressive inaccuracy below 80%)
Non-pulsatile flow (bypass)
Ambient light
Radiofrequency interference (MRI)

## Slide 21: Common ED Equipment & Procedures
  Thermometers
  Multiple toys and multiple equipment!
  Route
    Rectal, Oral, Auxiliary, Skin, Vascular, Naso-pharyngeal
  Infra-red, Thermocouple, Resistance Temp. Detector (RTD), and Thermistor
  Infrared  Portable, easy to use. Affected by ambient environment
  Rectal or Bladder  thermocouple device and infrared (via fibre optics)
  Errors  operator, locations, mixing types (oral, auxiliary, rectal, infrared on same sheet)
  Part of NEWS scoring

## Slide 22: Common ED Equipment & Procedures
Defibrillator
USES  Electrical current across the heart to convert VF/VT to Sinus rhythm
Important equipment in cardiac arrest management
Likelihood of correcting VF/pVT defibrillation is inversely proportional to time
  declines at 7-10% per min from onset of VF
Pacemaker function
Synchronised or non-synchronised shocks
Notes: Defibrillators • LITFL • CCC Equipment

## Slide 23: Common ED Equipment & Procedures
Some safety issues
  See ALS manual
    Sync mode functionality varies between products
    Familiarise oneself with machine prior to use
    Test how to “dump” unused charge

## Slide 24: Common ED Equipment & Procedures
Urine Dip
Detection limit set at 90%
Plastic strip with multiple testing agents
Colorimetric (visual and complemented by photometric analysis)
Ketone test: not all ketone bodies are tested.. False positive results
  What are ketone bodies?

## Slide 25: Common ED Equipment & Procedures
Video
  Demonstration video of urine dipstick analysis by CSW Kirsty and RN Karin

## Slide 26: Common ED Equipment & Procedures
Pregnancy b-HCG test
  Blood vs. urine
  Colorimetric test
  Present levels <5: negative
  Errors
    Biological variation
    Trophoblastic pregnancy
    Male positive
  All men with swollen tests should have a b-HCG test
    Why?

## Slide 27: Common ED Equipment & Procedures
Video
Demonstration of urine b- HCG test by CSW Kirsty and RN Karin

## Slide 28: Common ED Equipment & Procedures
BM/ blood glucose machine
  BM stands for Boehringer Mannheim, now part of Roche
  Some measure plasma glucose whilst others measure whole blood
  Change of strips allow blood ketone measurements
  Errors with readings
    Patient factors
    Equipment factors
    Operator factors

## Slide 29: Common ED Equipment & Procedures
Video
  Demonstration of BM machine by RN Karin and CSW Kirsty

## Slide 30: Common ED Equipment & Procedures
Blood gas/pH analysers:
  Electrodes to determine pH, CO-2, O-2,
Chemistry analysers:
  Used dry reagent pads
Electrolyte analysers:
  Use ion-selective electrode (ISE) to measure ion activity in the solution
Potentiometric analysers:
  Used External and Internal reference electrodes
Results could be networked or linked to EPRs
Blood gas machine  ABG/VBG

## Slide 31: Common ED Equipment & Procedures
References
  Non-invasive Blood Pressure • LITFL • CCC Equipment
  ECG Lead positioning • LITFL • ECG Library Basics
  Pulse Oximeter • LITFL • CCC Equipment
  Defibrillators • LITFL • CCC Equipment

## Slide 32: Common ED Equipment & Procedures
Acknowledgement
  RN Karin and CSW Kirsty gave permission for the creating of this video
Feedback
  robert.ritchie4@nhs.net
  nirasha.pinto1@nhs.net

## Slide 33: Common ED Equipment & Procedures
Summary
  Multiple equipment in ED
  Seek advice / support from colleagues if unsure
  Consider Safety to patient, oneself, and colleagues when using equipment

## Slide 34: Common ED Equipment & Procedures
Questions?
Feedback
  robert.ritchie4@nhs.net
  nirasha.pinto1@nhs.net